## Slide 1: EECS 388 Final Project
Jackson Yanek & Ian Collins

## Slide 2: HiFive
Proximity Sensor
  Simulates automatic braking system in vehicles
  Changes the on-board LED according to the output of the Lidar Sensor
Servo Motor
  Simulates steering wheel of vehicle
  Turns servo motor according to the relative angle output from the DNN algorithm from the Pi

## Slide 3: Raspberry Pi
DNN Algorithm
  Parses the video to output the relative angle of the vehicle in said video
Communication with HiFive
  Uses the UART pins on the HiFive to send a serialized signal of the relative angle for the servo motor
  Converts angle data into serial data

## Slide 4: HiFive & Pi Communication
if count%4 == 0:
  ser1.write(deg)
  deg = str(int(deg)) + “\n”
  ser.write(bytes(deg))
  print(deg)
int read_from_pi(int devid){
char ser_bytes[20];
int final;
if (ser_isready(devid)) {
ser_readline(devid, 20, ser_bytes);
sscanf(ser_bytes, "%d", &final);
return final;
} return 0;
}
Sending the data packet to the HiFive requires the angle data to be converted to a binary representation. Each angle is handled a byte at a time for the HiFive to interpret into movements for the servo motor.

## Slide 5: Obstacles Overcame
Byte representation
  Determining how the Pi would send serialized data to the HiFive took multiple iterations of how the Pi sends the data and how the HiFive receives the data
  HiFive reads the data as an decimal integer i.e. takes the whole number representation of the serial data
  Pi sends the data as a way that can be printed by the console and interpreted by the HiFive
Version Control
  We utilized Git to save our progress on our project which caused some version merge errors between our versions of the project